## Slide 1: Model Decomposition for Subtractive Manufacturing

## Slide 2: Introduction
CNC-Rapid Prototyping (CNC-RP) is subtractive manufacturing of parts
Part is rotated until all surfaces have been machined
Depends on axis selection for visibility
Implementing Rapid Prototyping Using CNC Machining (CNC-RP) Through
a CAD/CAM Interface, Frank 2007

## Slide 3: CNC-RP vs. Traditional CNC Machining
Pros
Toolpaths are automatically created
  Saves many hours to days of skilled labor time
Automated setup changes
Cons
Some geometries cannot be manufactured
Manufacturing process is slow compared to full production
Surface finish is better than 3d printing

## Slide 4: CNC-RP Failing Geometry
Undercut features (requires line of sight from tool)
Features not perpendicular to an axis of rotation
Notes: On the left we have undercut features. The red colored rectangles are not accessible with traditional machining processes.
On the right, we have three features which are perpendicular. The sides of the pockets can only be touched with a tool which is perpendicular to the pocket. This would require three setup orientations, as seen by the arrows. A limitation of the process is that you must rotate the entire model around a single axis. Picking one of the arrows as an axis, we are unable to manufacture that face.
If there was a way to break the part into multiple smaller pieces, each of which fit the criteria for CNC-RP manufacturing, they could be reassembled at the end.

## Slide 5: Octree Decomposition
Start with original model
Cut model in half on x, y, and z midplanes
Continue until stopping condition
  Typically size or attribute of cube
  In this case, it’s a Boolean (CNC-RP manufacturable?)
By WhiteTimberwolf, PNG version: Nü - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=9851485
Notes: There are a variety of ways which could be used to break the assembly up. One is octree decomposition. A model is broken into smaller chunks, and this continues until we meet criteria to stop subdividing. In this case, we want each chunk to be manufacturable by CNC-RP individually. Once this is achieved, we can look at the possibility of combining some pieces together so we don’t end up with lots of small pieces.

## Slide 6: Implementation Goals
Visualize the process of cutting the part into chunks
Allow user interaction to select chunks for separation

## Slide 7: Concept – Cutting Plane
User selects cutting plane
  Keyboard input x, y, or z
Cutting plane appears
User confirms choice by hitting the same button again

## Slide 8: Concept – Cutting Plane
User changes selected cutting plane

## Slide 9: Concept – Cut model
User confirms cutting plane
Object is separated

## Slide 10: Concept – Selected item
Models are textured simply at first
When a portion of the model is selected, another texture will be added

## Slide 11: Current Progress
Notes: Currently I have .obj models loading, but am running into some challenges going from here:
The textures I have made are not being applied to the objects. Textures are .bmp files, and the texture coordinates were mapped in Blender